## Slide 1: Department of Collegiate and Technical Education
Familiarization of PLC Installation Practices, troubleshooting and programming
(Week 4)
Session 1 : PLC Installation Practices, Editing,
and Troubleshooting
Automation & Robotics( V Semester)
Electronics and Communication Engineering
Electronics and Communication Engineering – 20EC53I

## Slide 2
Table of Content
PLC Installation Practices, Editing and Troubleshooting
PLC Enclosures, Electrical Noise, Leaky inputs and outputs, Grounding
Voltage variations and Surges program, Editing and Commissioning
Preventive Maintenance
Electronics and Communication Engineering – 20EC53I

## Slide 3
Electronics and Communication Engineering – 20EC53I
Programmable Logic Controller (PLC)
A PLC is a special form of microprocessor-based controller.
The adoptability to different control system and ability to modify/rewrite programs made PLCs flexible, cost effective system.

## Slide 4
Electronics and Communication Engineering – 20EC53I
PLC Enclosures
Programmable logic controllers (PLCs) require protection against temperature extremes, humidity, dust, shock, and vibration or corrosive environments.
An enclosure is the chief protection from atmospheric conditions.

## Slide 5
Electronics and Communication Engineering – 20EC53I
Electrical Noise
Noise, also called electromagnetic interference
EMI may be either radiated or conducted.
Noise usually enters through input, output, and
power supply lines.

## Slide 6
Electronics and Communication Engineering – 20EC53I
The following reduce the effect of electrical interference
Manufacturer design features
Proper mounting of the controller within an enclosure
Proper equipment grounding
Proper routing of wiring
Proper suppression added to noise generating devices

## Slide 7
Electronics and Communication Engineering – 20EC53I
Leaky Inputs and Outputs

## Slide 8
Electronics and Communication Engineering – 20EC53I
Grounding

## Slide 9
Electronics and Communication Engineering – 20EC53I
Voltage Variations and Surges
Isolation transformers are used in some PLC systems to isolate the PLC from electrical disturbances generated by other equipment connected to the distribution system.
The metal oxide varistor (MOV) surge suppressor, is the most popular surge protection device.

## Slide 10
Electronics and Communication Engineering – 20EC53I
Program Editing and Commissioning
Editing is simply the ability to make changes
commissioning, involves a series of tests to ensure

## Slide 11
Electronics and Communication Engineering – 20EC53I
* The general steps to be
followed when commissioning
a PLC system *

## Slide 12
Electronics and Communication Engineering – 20EC53I
Preventive Maintenance
Filters that have been installed in enclosures should be cleaned
Ensuring that the enclosure door is kept closed
Loose connections may result not only in improper function of
the controller but also in damage to the components of the
system.
To avoid injury to personnel and to prevent equipment damage,
connections should always be checked with power removed
from the system.

## Slide 13
Electronics and Communication Engineering – 20EC53I
Troubleshooting
In the event of a PLC fault, you should employ a careful and systematic approach to troubleshoot the system to resolve the problem.
The source of a problem can generally be narrowed down to the processor module, I/O hardware, wiring, machine inputs or outputs, or ladder logic program.

## Slide 14
Electronics and Communication Engineering – 20EC53I
Processor Module
The processor is responsible for the self-detection of potential problems.
The sample diagnostics LEDs found on a processor module.
What they indicate can be summarized as follows:

## Slide 15
Electronics and Communication Engineering – 20EC53I
RUN (Green)
On steady indicates that the process is in the RUN mode.
Flashing during operation indicates that the process is transferring a program from RAM to the memory module.
Off indicates that processor is in a mode other than RUN

## Slide 16
Electronics and Communication Engineering – 20EC53I
FLT (Red)
Flashing at power - up indicates that the processor has not been configured.
Flashing during operation indicates a major error either in the processor, chassis, or memory.
On steady indicates that a fatal error is present (no communications)
Off indicates there are no errors.

## Slide 17
Electronics and Communication Engineering – 20EC53I
BATT (Red)
On steady indicates the battery voltage has fallen below a threshold level, or the battery is missing or not connected.
Off indicates that the battery is functional.

## Slide 18
Electronics and Communication Engineering – 20EC53I
Input Malfunctions
If the controller is operating in the RUN mode but output devices do not operate as programmed, the faults could be associated with any of the following:
• Input and output wiring between field devices and modules
• Field device or module power supplies
• Input sensing devices
• Output actuators
• PLC I/O modules
• PLC processor
The steps taken can be summarized

## Slide 19
Electronics and Communication Engineering – 20EC53I
Output Malfunctions modules:
If the blown fuse indicator is not illuminated (fuse OK), then check to see if the output device is responding to the LED status indicator.
An output module’s logic status indicator functions similarly to an input module’s status indicator. When it is on, the status LED indicates that the module’s logic circuitry has recognized a command from the processor to turn on.

## Slide 20
Thank you
Electronics and Communication Engineering – 20EC53I
SMITHA SHENOY | SL. GR. Lecturer | Moderator | 111, GOVT. POLYTECHNIC, CHANNAPATNA
HEMANTH RAJU G H | SL.GR.Lecturer | Subject expert | 149, GOVT POLYTECHNIC, CHITRADURGA
NAGASHREE N | Sr.Gr. Lecturer | Content Developer | 110, DACG GOVT POLYTECHNIC, CHIKKAMAGALURU
VANITHA M H | Sr.Gr. Lecturer | Content Developer | 116, GOVT POLYTECHNIC, K R PETE
ASMATH | Sr.Gr. Lecturer | Content Developer | 116, GOVT POLYTECHNIC, K R PETE