## Slide 1
Syllabus: Variable Frequency Drive (VFD)
• VFD with motor control panel
• Modules of VFD
• Industrial and domestic applications of VFDs..

## Slide 2: VFD Panel
In most of the situations the industrial work space is dusty, dirty, wet, humid, corrosive, or hot.
In such harsh environments, it is not recommended and safe to mount the VFD exposed.
A VFD Control panel (an enclosure that protects the VFD and other electric components) can be used.
What is a VFD control panel used for?
Keeping all components in one panel
Keeping dust, dirt, and weather out of electrical parts
A complete motor control solution (bypass, harmonic filtering, etc.)

## Slide 3: Inside VFD Panel
VFD – The main component of the motor control panel. The VFD inside will vary in voltage, horsepower, full load amps (FLA), and other specifications. Sometimes you may find redundant VFDs installed in case of a VFD failure.
Line reactors – 3% or 5% to reduce harmonic distortion
Harmonic filters – a more effective way to reduce harmonic distortion
Circuit breaker – protects the electrical circuit from overload or short circuit
Bypass – keeps the system running even if the VFD fails
PLC – Programmable Logic Controller – for more advanced operations

## Slide 4: Inside VFD Panel (Contd…)
Modem – for communication purpose
AC or other cooling units – keeps the panel at a certain temperature depending on surrounding environment
Soft-starter – starts motor slowly but without speed control
Surge protector – protects the system from voltage spikes
Multiple motor overloads – an option for powering multiple motors off one VFD, typically used on fan walls
Anti-condensation heater (available in NEMA 3R panels) – eliminates the buildup of dew inside the VFD panel
Motor starters – for running motors across the line

## Slide 5: Application of VFD drives
The industrial applications include,
Extruders: A machine that shapes material by forcing it through a specially designed opening
Electric cranes
Roller coasters
Mechanical bulls

## Slide 6: Application of VFD drives
The commercial applications include
Pumps to control flow and even volume in a tank
Lifts and escalators
Swimming pool filtration system
The Domestic applications include
Washing Machines
Water pumps
As Pressure booster pumps to supply adequate pressure to terminal units such as showers and bathrooms in apartments